ALGORITHM FOR RUNGE-KUTTA NUMERICAL KINETICS UP TO 4TH-ORDER
(See Rao, Singiresu. Applied Numerical Methods for Scientists and Engineers. Prentice-Hall, Upper Saddle River, NJ, pp. 654-655.)

Variable Explanation:
Let m, n index orders of approximation
Let p index a chemical specie
Let u, w index reaction steps, forward or reverse
Let i, i+1 index time steps
Let C_p (t_i) be the concentration of specie p at time i
Let C_p^(n) be the nth order interpolation correction to concentration of p
Let V_u^(n) be the velocity of reaction step u to the nth order
Let R_p^(n) be the nth order correction to rate of production of p
Let k_u be the rate constant of step u
Let v_{pw} be the signed (- for reactants, + for products) stoichiometric coefficient of p in step w
Let T_p be the threshold at which a specie p behaves as if it were soluble in the medium
Let S_p be the sharpness of the arctangent compensation curve of specie p

Cash-Karp Parameters for Embedded Runge-Kutta Method
matrix{ n # {} # {} # b_{n,m} # {} # {} # c_n # c_n^"*" ## 1 # {} # {} # {} # {} # {} # 37 over 378 # 2825 over 27648 ## 2 # 1 over 5 # {} # {} # {} # {} # 0 # 0 ## 3 # 3 over 40 # 9 over 40 # {} # {} # {} # 250 over 621 # {18575 over 48384} ## 4 # 3 over 10 # -9 over 10 # 6 over 5 # {} # {} # 125 over 594 # {13525 over 55296} ## 5 # -11 over 54 # 5 over 2 # -70 over 27 # 35 over 27 # {} # 0 # 277 over 14336 ## 6 # 1631 over 55296 # 175 over 512 # 575 over 13824 # 44275 over 110592 # 253 over 4096 # 512 over 1771 # 1 over 4 ## ital "m=" # 1 # 2 # 3 # 4 # 5 # {} # {} }
Algorithm for Embedded Runge-Kutta-Fehlberg Method

for i=0 to max time for some Δt
for each order, n, up to 5
for each step, u

// decide how much to weight the velocity based on transition and threshold
// note that heterogeneous species do not normally contribute to rate
H_b = left lbrace matrix{ 0 # homogeneous ## 1 # ital "none", C_p (t_{i-1}) > T_p ## {{C_p (t_{i-1})} over T_p} # linear, C_p (t_{i-1}) < T_p ## {{arctan( S_p times { ({C_p (t_{i-1})} over T_p - 0.5 )}~)} - arctan( -0.5 times S_p )} over { arctan( 0.5 times S_p ) - arctan( -0.5 times S_p ) } # atan, C_p (t_{i-1}) < T_p } right none

// calculate the velocity for each step based on the rate const and the prev concs
// forward based on k+ and reactants, reverse on k- and products
V_{u}^{(n)} = k_{u}prod from{p} to{ital "in " u} ( H_b + (1-H_b)C_{p}^{(n-1)} )
next step

for each species, p

// total rates from each step to each specie
R_{p}^{(n)} = sum from{w} to {involving p} {v_{pw}(V_{w,plus}^{(n)} - V_{w, minus}^{(n)})}
// calculate correction values for next velocity calculation
C_{p}^{(n)} = C_{p}^{(0)} + %DELTA t sum from m=1 to n {b_{(n+1),m}R_p^(m)}
// correct the concentration based on new rate values*
C_p (t_i) ital "+=" %DELTA t c_n R_p^(n)
// calculate the error for the current step**
%DELTA_p ital "+=" %DELTA t ( c_n - c^"*"_n ) R_p^(n)
next species
next order
if %DELTA_[p] > %DELTA_ideal then %DELTA t "::=" %DELTA t times lline {%DELTA_ideal over %DELTA_[p]} rline ^ 0.25 ital "and retry" newline alignr else %DELTA t "::=" %DELTA t times lline {%DELTA_ideal over %DELTA_[p]} rline ^ 0.2 ital "and continue"
next timestep
* Overall: C_p (t_i) = C_p (t_{i-1}) + %DELTA t sum from n=1 to {max n} {c_n R_p^{(n)}}
** Overall: %DELTA_p = %DELTA t sum from n=1 to {max n} { (c^"*"_n - c_n) R_p^{(n)}}